## Slide 1: Surface-Atmosphere Fluxes Part II
Christine Wiedinmyer
christin@ucar.edu

## Slide 2: Part II
What did we just learn?
  What is emitted?
  What are emission sources?
How is it applied?
  Why do we need to know emission rates?
  How do we apply measured emissions?
  How do we calculate emissions?
  EXAMPLE
    Fire Emissions

## Slide 3: Emissions to the atmosphere
Volatile Organic Compounds (VOC)
Nitrogen Species
  NOx
  NH3
Carbon monoxide
Sulfur species (SO2)
Particles
  Chemistry
  Physical properties

## Slide 4: Emission Sources
Natural (Biogenic/Geogenic)
  Lightning (NOx) N2 NOx
  Volcanoes (SO2, aerosols)
  Oceans
  Vegetation
  * Highly variable in space and time, influenced by season, T, pH, nutrients…
Anthropogenic
  Mobile sources
  Industry
  Power generation
  Agriculture
FIRE

## Slide 5: How much comes from these sources?

## Slide 6
Global Emission Estimates:
Trace Gases
EDGARFT2000
Yan et al, GBC, 2005
Guenther et al., 1995; 2006; pers. comm.
GFEDv2
Andreae and Merlet, GBC, 2001
Yokelson et al., ACP, 2008

## Slide 7
Global Emission Estimates:
Particles
Andreae and Rosenfeld, Earth Science Reviews, 2008

## Slide 8
Andreae and Rosenfeld, Earth Science Reviews, 2008

## Slide 9: Location Matters!
Bronnimann et al., Meteorologische Zeitschrift, 2009

## Slide 10
Andreae and Rosenfeld, Earth Science Reviews, 2008

## Slide 11
Satellite Data from OMI

## Slide 12: Timing matters, too
Daily and seasonal trends in emissions have important implications on chemistry and air quality
For example: Why are you asked to fill up your gas tank in the evening during the summer smog season?

## Slide 13
Tropospheric ozone forms in the presence of NOx, VOC and sunlight
Takes time to make (peaks in summer afternoon)
Emissions in morning contributes to daytime formation of ozone

## Slide 14: Example: Emissions from fires
Courtesy of Brian Magi, NOAA GFDL

## Slide 15: What is emitted from fires?
Urbanski et al., Wildland Fires and Air Pollution, 2009

## Slide 16: What else do we need to consider?
Controlling variables:
- weather
- what burns
- how it burns
- where it burns
- when it burns

## Slide 17
  A(x,t): Area burned
  B(x,t): Biomass burned (biomass burned/area)
    type of vegetation (ecology)
    fuel characteristics:
      amounts of woody biomass, leaf biomass, litter, ...
    fuel condition
      moisture content
  Efi: Emission factor (mass emissioni /biomass burned)
    fuel characteristics
    fuel condition

## Slide 18
  (1) Emissions determined from field measurements
Thomas Karl, NCAR
TROFFEE Study, Brazil

## Slide 19
Deforestation Fire in the Yucatan, Mexico (March 2006)
Bob Yokelson, UMT
http://www.umt.edu/chemistry/faculty/yokelson.htm

## Slide 20: Emission Ratios
Andreae and Merlet, Global Biogeochemical Cycles, 2001
Example: CH3Cl

## Slide 21
A schematic of the USFS Fire Sciences Laboratory (FSL)
combustion facility in Missoula, MT.
http://www.umt.edu/chemistry/faculty/yokelson.htm
  (2) Fire emissions determined from laboratory experiments

## Slide 22: Getting at Emission Factors…
Mx Amount of compound released
Mbiomass Amount of biomass burned
Mc Mass of carbon emitted
[C]biomass Carbon concentration in biomass burned (45%)
[x] Concentration of species x in the smoke
[Ci] Concentration of species i in the smoke
Andreae and Merlet, Global Biogeochemical Cycles, 2001

## Slide 23: Measurements  Models
EFx Emission factor for species X
ER(X/Y) Emission ratio of species X relative to the reference species Y
MWx Molecular weight of species X
MWY Molecular weight of species Y
EFY Emission factor of species Y
Andreae and Merlet, Global Biogeochemical Cycles, 2001

## Slide 24: Measurements of Organic Compounds in Plumes
Canisters
  Analysis back at home (GC-FID, GC-MS, etc.)
FTIR
  E.g., Yokelson et al., University of Montana
PTR-MS
  E.g., Karl et al., NCAR

## Slide 25
Akagi et al., Atmos. Phys. & Chem Disc., 2010

## Slide 26: Other controlling variables
Vegetation burned
Location/timing
Fire severity

## Slide 27
  A(x,t): Area burned
  B(x,t): Biomass burned (biomass burned/area)
    type of vegetation (ecology)
    fuel characteristics:
      amounts of woody biomass, leaf biomass, litter, ...
    fuel condition
      moisture content
  Efi: Emission factor (mass emissioni /biomass burned)
    fuel characteristics
    fuel condition

## Slide 28
GLOBAL
Northern Hemisphere
Southern Hemisphere
Daily Emission estimates of non-methane organic compounds from fires
Wiedinmyer et al, Geosci. Model Dev. Discus., 2010

## Slide 29
Wiedinmyer et al, Geosci. Model Dev. Discus., 2010

## Slide 30
Fire Emissions
Variability:
Spatial
Temporal
Wiedinmyer and Neff, Carbon Balance and Management, 2007

## Slide 31: Example: Mobile Source Emissions
What are ways that mobile sources emit gases and particles to the atmosphere?
  Tailpipe emissions
  Road dust
  Evaporative emissions
  Pumping gas

## Slide 32: What needs to be considered?

## Slide 33
U.S. EPA provides documentation for developing emission inventories

## Slide 34: Summary
Estimates of emissions are very important
Not all sources are equal
Timing and location matter
Lots of uncertainty associated with emission estimates